## Slide 1
VARIATIONAL MODE DECOMPOSITION
From VMD to unfolded VMD
The ADMM solver, its deep-unfolded version UVMD (Ahmad et al., 2025), where it falls short in theory, and a three-dataset comparison at K = 13
Aitzaz · SPML group, Aarhus University · October 2026
Notes: Plan: classic VMD, the idea of unfolding, UVMD in detail, theoretical caveats, then reconstruction and separation results on synthetic, CWRU and LargeST data.

## Slide 2
What this talk covers
1
Classic VMD
The problem, the ADMM updates, how the loop runs
2
Deep unfolding
Iterations become layers, hyperparameters become weights
3
UVMD (Ahmad et al.)
Layer, trained parameters, training, paper versus code
4
Where it falls short
Theoretical caveats and how far ω moves in practice
5
Results
Reconstruction, then separation: synthetic, CWRU, LargeST

## Slide 3
CLASSIC VMD
VMD: split a signal into K narrow-band modes
CONSTRAINED PROBLEM
min over {u_k}, {ω_k}
Σ_k ‖ ∂t[(δ(t) + j/(πt)) ∗ u_k(t)] · e^(−jω_k t) ‖²
subject to Σ_k u_k = f
Reading the terms
u_k: mode k, ω_k: its centre frequency
Hilbert term: makes u_k analytic, one-sided spectrum
e^(−jω_k t): shifts mode k to baseband
‖∂t ·‖²: the bandwidth of that shifted mode
Constraint: the modes must add up to f
Hyperparameters: number of modes K, bandwidth penalty α, dual step τ.
Notes: VMD minimises the summed bandwidth of K modes, each centred on its own frequency, under the constraint that the modes reconstruct the signal exactly.

## Slide 4
CLASSIC VMD
ADMM turns it into three closed-form updates
Mode update
û_k = ( f̂ − Σ_{i≠k} û_i + λ̂/2 ) / ( 1 + 2α(ω − ω_k)² )
Centre frequency
ω_k = ∫₀^∞ ω |û_k(ω)|² dω / ∫₀^∞ |û_k(ω)|² dω
Dual ascent
λ̂ ← λ̂ + τ ( f̂ − Σ_k û_k )
The mode update is a Wiener-like filter centred on ω_k; α sets how narrow it is
ω_k is the power-weighted mean frequency of the mode, positive half spectrum
All updates run in the FFT domain, so the method is global and non-causal
Notes: Standard VMD (Dragomiretskiy and Zosso, 2014). In our benchmark tau is 0, so the multiplier stays at zero.

## Slide 5
CLASSIC VMD
How the VMD loop runs
START
Initialise
ω_k on a uniform grid, û = 0, λ̂ = 0
→
STEP 1
Modes
Update û_k for k = 1..K, one after the other
→
STEP 2
Centres
ω_k from the mode’s power spectrum
→
STEP 3
Multiplier
Dual ascent on λ̂ with step τ
Repeat until the modes stop changing (tolerance) or the iteration cap is reached. Typically hundreds of FFT sweeps per signal.
K = 13
α = 2000
τ = 0
tol = 1e-7
max 499 iterations
DC mode, mirrored extension
Notes: Settings in the pills are the ones used in this benchmark. The mode sweep is Gauss-Seidel.

## Slide 6
DEEP UNFOLDING
Unfolding: an iterative algorithm becomes a network
ITERATIVE SOLVER
repeat n = 1..500:
x ← T(x; θ)
One operator T, one fixed θ (α, τ), many repetitions until convergence.
UNFOLDED NETWORK
x₁ = T(x₀; θ₁)
x₂ = T(x₁; θ₂)
… x_N = T(x_{N−1}; θ_N)
N copies (N small), each with its own learnable θ_n.
Each iteration becomes a layer; fixed depth N replaces “until convergence”
Hyperparameters become weights that gradient descent can tune
Origin: LISTA, which unfolded ISTA for sparse coding (Gregor and LeCun, 2010)
Notes: The structure of the algorithm is kept, so the network stays interpretable: every layer is still one step of the original method.

## Slide 7
DEEP UNFOLDING
How an unfolded algorithm is trained
1
Truncate
Keep N iterations, N = 1 or 2 here
2
Parametrise
Pick hyperparameters to learn, one set per layer
3
Define a loss
Score the output of the last layer
4
Backpropagate
Gradients flow through all layers; Adam updates the parameters
5
Fix and deploy
Freeze the weights, run N layers on new signals
TRADE
Speed for guarantees
Far fewer steps, but no convergence guarantee and tuned to the training data
Notes: Training is end to end: the loss only sees the final layer, but its gradient reaches every layer’s parameters.

## Slide 8
UVMD (AHMAD ET AL.)
UVMD: one layer is one VMD sweep
Input f
Mirror, FFT, keep the positive half: f̂₊
→
Layer 1
α_k, λ̂₁
→
Layer N
α_k, λ̂_N
→
Modes u_k
Inverse FFT; loss on Σ_k û_k
û_k = ( f̂₊ − Σ_{i≠k} û_i − λ̂_n/2 ) / ( 1 + softplus(α_k)(ω − ω_k)² )
ω_k = Σ ω |û_k|² / Σ |û_k|² (positive half, k ≥ 1)
Layer n sweeps through the K modes (Gauss-Seidel), then recomputes every ω_k from the new spectra. Mode 0 stays at DC. Written as in the released code.
Notes: Source: Ahmad, Wesemann, Waschkowski, Khalid, arXiv 2509.00703, and the released code (OsamaAhmad369/MAGN, uvmd.py). The equation form is the code’s; the paper differs slightly.

## Slide 9
UVMD (AHMAD ET AL.)
What UVMD trains, and what it does not
TRAINED
α_k, K values
• Bandwidth penalty per mode, through softplus
• Shared by all layers
• Initialised at 2000
TRAINED
λ̂_n, one per layer
• Complex vector of length 2T (T = signal length)
• Replaces the dual variable
• Initialised at 0
NOT TRAINED
ω_k
• Recomputed from û_k in every layer
• Starts on a fixed uniform grid, 0.5·k/K
• No weight of its own
Both trained parameters enter only the mode update. The frequency update has none, so ω can change only through û_k.
Notes: The released code allocates N+1 rows for lambda; the last is never used. Alpha is one vector of K values reused in every layer.

## Slide 10
UVMD (AHMAD ET AL.)
How UVMD is trained
Item | Setting
Loss | Spectral reconstruction error, Σ ¦Σ_k û_k − f̂₊¦ (L1 in the code, L2 in the paper)
Supervision | None: no ground-truth modes, the loss sees only the sum
Optimiser | Adam, learning rate 0.1, batch size 1
Schedule | Up to 100 epochs, early stopping with patience 10
Data split | 70 / 15 / 15, random_state 42
Model size | K = 13 modes, N = 1 or 2 layers
Initial values | α_k = 2000, λ̂ = 0, ω on the uniform grid
The learned α and λ̂ are shared by every signal of the dataset; they are not computed per signal.
Notes: We use the upstream training loop unchanged. Upstream saves the best weights and then overwrites them with the last-epoch weights; the training loss was still falling at epoch 100.

## Slide 11
UVMD (AHMAD ET AL.)
The paper and the released code differ
Item | Paper | Released code
Denominator | 1 + 2·softplus(α)(ω − ω_k)² | 1 + softplus(α)(ω − ω_k)²
Multiplier term | + λ̂/2 | − λ̂/2
Loss | L2 norm | L1, sum of absolute values
Problem statement | No constraint, no λ update given | λ̂ is a free trained tensor
The sign of λ̂ is absorbed by training, but the factor 2 changes what α means: the same number gives a different filter width
The headline “250× faster” is about 162× from the paper’s own timings
“Robust” is in the title, but no noise experiments are reported
The upstream repository carries no licence
Notes: We use the released code unchanged as the reference implementation.

## Slide 12
CAVEAT 1
The trained parameters never act on ω
α_k, λ̂
The only weights
→
û_k update
Filter width and offset
→
ω_k update
Mean frequency of û_k, no weight
ω can move only indirectly, through the spectrum that α and λ̂ shape
With N = 1 or 2 it is updated once or twice; classic VMD updates it hundreds of times
It starts on a uniform grid that need not match the signal’s true frequencies
Nothing in the loss pushes ω toward the right place
Notes: Our measurements on the next slides show this holds on traffic and synthetic data, but not on CWRU.

## Slide 13
CAVEAT 2
The loss rewards reconstruction only
λ̂ is a free complex vector of length 2T: it can absorb the residual and cut the error without making better modes
α can collapse: with α → 0 a mode passes everything and the sum is exact
No term asks for orthogonal or narrow-band modes
One α and λ̂ for the whole dataset; changing T means retraining
SEEN ON CWRU, 1 LAYER
Reconstruction error
0.0662 → 0.0004
Spectral overlap
0.066 → 0.371
Untrained VMD-1 to trained UVMD-1. One α went to 0.
Notes: The CWRU result is the clearest case: near-perfect reconstruction with modes that overlap far more than the untrained ones.

## Slide 14
FURTHER CAVEATS
Other limits to keep in mind
Far from the fixed point
1 or 2 sweeps cannot reach what 500 reach, so the output is not a VMD solution
Non-causal
A global FFT sees the whole window, so forecasting use risks leakage from the future
Fixed window length
λ̂ has length 2T, so a different T needs new training
Batch size 1
One signal per step, so a GPU helps little
Training bookkeeping
Best weights are saved, then overwritten by the last epoch; loss still falling at epoch 100
Not tuned for forecasting
The paper reports that more layers overfit

## Slide 15
Does ω really barely move? Partly
Mean shift | VMD | UVMD-1 | UVMD-2
Synthetic | 0.46 | 0.69 | 0.46
CWRU | 0.62 | 1.86 | 2.05
Traffic | 1.61 | 0.38 | 0.28
Grid spacings from the start grid; VMD is the converged run.
Traffic and synthetic: UVMD moves ω little, as predicted
CWRU: UVMD moves it 3× more than converged VMD
Moving more is not moving right: synthetic centre-frequency error is 0.0025 for UVMD-1 against 0.0011 for VMD
Notes: Shift is in grid spacings of 0.5/K cycles per sample, averaged over modes 1 to K-1 and over test signals. Converged VMD is computed on 10 signals.

## Slide 16
RESULTS
Experimental setup
Synthetic
4 known modes, ground truth available, 30 test signals
CWRU bearing
Vibration with fault lines, 300 test signals
LargeST traffic
San Diego sensors, bounded run, 30 test windows
Methods, all at K = 13: converged VMD; VMD-N (VMD stopped after N iterations); trained UVMD-N with N = 1, 2.
VMD-N equals UVMD-N before training, so the pair isolates the effect of training.
Reconstruction: relative error ‖x − Σu_k‖ / ‖x‖.
Separation, without ground truth: orthogonality index, spectral overlap, relative bandwidth, energy ratio, with the effective number of modes as a guard.
Notes: The traffic run uses 100 training, 20 validation and 30 test nodes; the full protocol has not been run.

## Slide 17
RESULTS
Reconstruction: trained UVMD wins
Relative error ↓ | VMD converged | VMD-1 | UVMD-1 | VMD-2 | UVMD-2
Synthetic | 0.0294 | 0.0499 | 0.0066 | 0.0379 | 0.0142
CWRU | 0.0760 | 0.0662 | 0.0004 | 0.1070 | 0.0004
LargeST traffic | 0.0303 | 0.0729 | 0.0205 | 0.0838 | 0.0372
Trained UVMD-N beats untrained VMD-N on 100% of signals in every dataset and for both depths
One trained layer also beats converged VMD on all three datasets
Exception: on traffic, UVMD-2 (0.0372) is slightly worse than converged VMD (0.0303)
Notes: Mean over test signals. Bold marks the best entry of each row (tie on CWRU).

## Slide 18
RESULTS
How much training cuts the error
Trained UVMD-N error divided by untrained VMD-N error, same depth. Lower is better.
Synthetic
0.13×
1 layer
0.38×
2 layers
CWRU
0.01×
1 layer
<0.01×
2 layers
LargeST traffic
0.28×
1 layer
0.44×
2 layers
The gain is largest where the loss can be gamed most easily (CWRU, with one α driven to 0). Read these numbers together with the separation results.
Notes: Ratios of means from Table A2. CWRU 2 layers is 0.00 in the table, below rounding precision.

## Slide 19
RESULTS
How separation is measured without ground truth
Criterion | What it measures | Better
Orthogonality index | Σ_{i<j} ¦⟨u_i, u_j⟩¦ / ‖x‖², content shared between modes | lower
Spectral overlap | Share of spectrum two modes occupy together | lower
Relative bandwidth | Energy-weighted spectral width of a mode ÷ Nyquist | lower
Energy ratio | Σ‖u_k‖² / ‖x‖²; above 1 double counts, below 1 loses energy | closer to 1
Effective modes | 1 / Σ s_k², s_k the energy share of mode k; a guard, not a score | not near 1
On the synthetic data, where true modes are known, relative bandwidth tracks true separation best (Spearman −0.85), orthogonality and overlap about −0.5. Reconstruction error points the wrong way (+0.52).
Notes: Spearman correlation against grouped mode SNR over 150 points (30 signals by 5 methods). The energy ratio showed no relation (-0.14).

## Slide 20
RESULTS
Separation: training does not help
Converged VMD is best on orthogonality, overlap and bandwidth in all three datasets
Trained UVMD-1 never beats VMD-1 on bandwidth (0% of signals): 1.65× synthetic, 2.59× CWRU, 1.08× traffic
Overlap is worse after training in five of six dataset and depth pairs, level in the sixth
Energy ratio is the one criterion that improves
Notes: Lower is better for orthogonality, overlap and bandwidth. Ratios are trained UVMD-1 over untrained VMD-1 from Table A2.

## Slide 21
RESULTS
Synthetic data: separation against the true modes
Method | Mode SNR (dB) ↑ | Freq. error ↓
VMD converged | 20.7 | 0.00106
VMD-1 | 12.4 | 0.00120
UVMD-1 | 8.5 | 0.00252
VMD-2 | 18.8 | 0.00090
UVMD-2 | 7.3 | 0.00207
Training lowers the true mode SNR by 4 to 12 dB while reconstruction error falls by a factor of 2.7 to 7.6. Centre frequencies get farther from the truth.
Notes: Grouped mode SNR: each estimated mode is assigned to the true mode it projects onto most, and the assigned modes are summed. Frequency error is in cycles per sample.

## Slide 22
Conclusions and next steps
WHAT WE FOUND
UVMD reconstructs better than VMD at the same depth on every signal, with 1 or 2 layers instead of hundreds of iterations
It does not separate better: at best on par with untrained VMD-N, below converged VMD
Reconstruction error is no evidence of separation
ω barely moves on traffic and synthetic, but moves a lot on CWRU
NEXT STEPS
Add a separation term (bandwidth or orthogonality) to the loss
Give ω a trainable path: learned initial grid or a filter on the spectrum
Ablate: train α only, then λ̂ only
Test on forecasting with causal windows
Run the full traffic protocol
Traffic results come from a bounded run (100 / 20 / 30 nodes). Code, tables and figures: repository vmd-uvmd-comparison.
Notes: The next-step ideas are proposals, not results.